## Slide 1: SPB Optimization
1200 V DC-link, 300 kW three-phase inverter

## Slide 2: Optimizing SPB Level Number with Available GaN Devices
More cells
lower Vcell
better device FOM
more switches
Core question:
How many stacked two-level cells are worth adding before device count and control overload dominate?
Method:
Off-the-shelf GaN database
D-FOM screening
first-order loss model

## Slide 3: Why this optimization matters
System target
1200 V DC-link
• 300 kW output power
• ≈ 291 A rms phase current
• high-frequency GaN switching
SPB opportunity
Stacked cells let each GaN device block only a fraction of the DC-link voltage, opening low-voltage GaN devices with lower
SPB penalty
Each added cell brings six more switch positions, gate drivers, sensing, balancing, layout effort, and reliability questions.
Voltage stress
Device FOM
Loss & thermal
Complexity
The optimum is not simply the lowest-voltage device: it is the best balance of device FOM, conduction loss, switching loss, and implementation complexity.

## Slide 4: Screening workflow implemented in MATLAB
1. Inputs
VDC, Pout, pf, modulation, fsw, dv/dt, di/dt, safety factor
2. Database
RDS(on), Coss, voltage rating, current rating, vendor/device
3. Discrete levels
4. Loss model
Only realizable x-axis points are used: 650 V, 200 V, 150 V, 120 V, 100 V devices create different discrete SPB level counts.

## Slide 5: Preliminary Results
Top-left
Device database: lower-left is attractive, but voltage rating must be feasible.
Top-middle
D-FOM ranks devices by RDS(on)–Coss trade-off.
Top-right
Discrete level count chooses the feasible best-FOM devices.
Bottom row
Separates conduction, switching energy, and switching-loss components.

## Slide 6: Preliminary Results
Low voltage GaN often has excellent RDS(on), but its Coss can be large.
The optimum depends on current, voltage per cell, and switching frequency.
D-FOM alone does not decide the design.
It only decides which devices deserve closer evaluation.
Interpretation
100–200 V devices look attractive, but only become feasible when enough cells are stacked.

## Slide 7: Discrete levels: the x-axis is constrained by available device classes
650 V GaN
cells ≈ 3
simple, mature
200 V GaN
cells ≈ 8
Low voltage
100 V GaN
cells ≈ 15
Aggressive low-voltage
3
6
9
12
15
18
8
650V
200V
100V
If we force 14 cells with 100 V GaN, the voltage margin is only about 100 / (1200/15) = 1.25×.

## Slide 8: Loss model
What it captures
• higher cell count reduces Vcell
• lower-voltage devices reduce RDS(on)
• higher fsw amplifies switching energy
• dv/dt and di/dt affect VI overlap
What it still misses
• measured Eon/Eoff per device
• dynamic RDS(on)
• thermal impedance
• layout inductance and overshoot
• DC-link capacitor ripple
Next step: replace the generic overlap model with measured or datasheet-based Eon/Eoff for each candidate voltage class.

## Slide 9: Suggested comparative study for the project
Case A: simple high-voltage SPB
650 V GaN
3 cells
Mature devices, low cell count
Lower sensing and gate-drive overhead
Case B: aggressive low-voltage SPB
100 V GaN
15 cells
Case C: low-voltage SPB
200 V GaN
8 cells
Middle-ground baseline
Compare each case using the same current, fsw, thermal boundary, and modulation strategy.
Evaluation metrics
Semiconductor loss
conduction + Coss + measured/estimated Eon/Eoff
Cost / Failure rate *Normalized?
switch positions, gate drivers, isolated supplies, sensors
Thermal feasibility
junction rise at nominal and overload current
DC-link / module capacitor
ripple current, energy storage, balancing control
Motor friendliness
voltage steps, CM voltage, winding stress, filtering need

## Slide 10: References
J. A. Anderson, G. Zulauf, J. W. Kolar, and G. Deboy, “New Figure-of-Merit Combining Semiconductor and Multi-Level Converter Properties,” IEEE Open Journal of Power Electronics, 2020.
G. Rohner, J. W. Kolar, D. Bortis, and M. Schweizer, “Optimal Level Number and Performance Evaluation of Si/GaN Multi-Level Flying Capacitor Inverter for Variable Speed Drive Systems,” ICEMS, 2022.
G. Rohner et al., “Comparative Evaluation of Three-Phase Three-Level GaN and Seven-Level Si Flying Capacitor Inverters for Integrated Motor Drives Considering Overload Operation,” IEEE Access, 2024.
G. Rohner, J. Huber, S. Mirić, and J. W. Kolar, “Comparative Evaluation of Three-Phase Three-Level Flying Capacitor and Stacked Polyphase Bridge GaN Inverter Systems for Integrated Motor Drives,” Electronics, 2024.
“Literature Survey for Integrated Modular Motor Drives,” presentation.