## Slide 1: Common-Mode Voltage Reduction in Two-Level Inverters Using an Adaptive Carrier-Phase-Shift Method
Enes Ayaz, Shahriar Sarmast Ghahfarokhi, Staffan Norrga, Hans-Peter Nee – KTH Royal Institute of Technology
Introduction & Motivation
Two-Level Voltage Source Inverters dominate industrial motor drives due to simplicity, low cost, and reliability.
Problem: PWM outputs → Common-Mode Voltage → leads to:
Electromagnetic Interference (EMI)
Bearing currents → insulation damage → reduced lifespan
Existing Mitigation Approaches:
New inverter topologies / CM filters → ↑ cost & complexity
Constant carrier-phase-shift PWM → partial CMV reduction only
Key Idea:
Dynamically adjusts carrier phase shifts every switching interval
Minimizes CMV harmonics at the instantaneous level.
No hardware changes → scalable & low-cost.
Proposed Method
Represent 1st carrier harmonics of each phase in phasor domain.
Simulation Results
Test cases: = 0.4, 0.8.
FFT shows significant CMV harmonic reduction vs. conventional method.
Reduction observed across all modulation indices.
Analytical Investigation of CMV
CMV in 2L-VSI:
When conventional single-carrier SPWM is implemented, the phase-to-neutral voltages ( ) can be calculated as:
Harmonic decomposition → Zero-sequence components create CM currents.
Conventional Interleaving
Shifts carriers by 0°, 120°, 240° → redistributes harmonics.
Adjust phase shifts to either:
  Form a triangle → cancel CMV completely
  Align small vectors opposite to the largest vector (triangle inequality not met)
Algorithm
Discussion
  Bearing current mechanisms: capacitive, electric discharge machining (EDM), and circulating bearing currents.
  Capacitive bearing currents: strongly influenced by high-frequency CMV components; higher dv/dt → larger currents.
  EDM currents: triggered when CMV exceeds lubricant breakdown voltage → electrical discharge across bearings.
  Switching pattern impact: less critical for capacitive currents but important for EDM current suppression.
= 0.8
Experimental Results
Conclusion
Adaptive Carrier-Phase-Shift SPWM:
Reduces instantaneous CMV more effectively than fixed-phase methods.
Maintains simplicity of 2L-VSIs
No additional hardware required
Future Work:
Extend to multi-phase & multi-level inverters
Funded by EU CHIPS JU (PowerizeD) & Swedish Energy Agency (HEMIZERO)
= 0.4
= 0.8
= 0.4