## Slide 1: Common-Mode Voltage Reduction in Two-Level Inverters by Introducing Adaptive Carrier-Phase-Shift Method
Enes Ayaz, Shahriar Sarmast Ghahfarokhi, Staffan Norrga, Hans-Peter Nee – KTH Royal Institute of Technology
Introduction & Motivation
Two-Level Voltage Source Inverters dominate industrial motor drives due to simplicity, low cost, and reliability.
Problem: PWM outputs → Common-Mode Voltage → leads to:
Electromagnetic Interference (EMI).
Bearing currents → insulation damage → reduced lifespan.
Existing Mitigation Approaches:
New inverter topologies / CM filters → ↑ cost & complexity.
Constant carrier-phase-shift PWM → partial CMV reduction only.
Key Idea:
Dynamically adjusts carrier phase shifts every switching interval.
Minimizes CMV harmonics at the instantaneous level.
No hardware changes → scalable & low-cost.
Proposed Method
Represent 1st carrier harmonics of each phase in phasor domain.
Simulation Results
Analytical Investigation of CMV
CMV in 2L-VSI:
When conventional single-carrier SPWM is implemented, the common-mode voltage ( ) can be calculated as:
Harmonic decomposition → Zero-sequence components create CM currents.
Conventional Interleaving
Shifts carriers by 0°, 120°, 240° → redistributes harmonics.
Adjust phase shifts to either:
  Form a triangle → cancel CMV completely.
  Align small vectors opposite to the largest vector (triangle inequality not met).
Algorithm
Discussion
  Bearing current mechanisms: capacitive, electric discharge machining (EDM), and circulating bearing currents.
    Capacitive bearing currents: strongly influenced by high-frequency CMV components; higher dv/dt → larger currents.
    EDM currents: triggered when CMV exceeds lubricant breakdown voltage → electrical discharge across bearings.
  Switching pattern impact: less critical for capacitive currents but important for EDM current suppression.
Experimental Results
Conclusion
Adaptive Carrier-Phase-Shift SPWM:
Reduces instantaneous CMV more effectively than constant carrier phase-shift PWMs.
Maintains simplicity of 2L-VSIs.
No additional hardware required.
Future Work:
Extend to multi-phase & multi-level inverters.
Funded by EU CHIPS JU (PowerizeD) & Swedish Energy Agency (HEMIZERO)
Fig.1 :The system structure of a 2L-3Ph motor drive system.
Table. 1 : Frequency Components and Their Sequences Around First Carrier Harmonic.
Table. 2 : Frequency Components and Their Phases Around First Carrier Harmonic for Multi-Carrier Signals.
Fig.2 :Phasor domain analysis of the CMV in the first switching harmonic. a) The phase voltages. b) The CMV.
Fig.3 :Determination of the carrier phase shifts in phasor domain analysis. a) Triangle formation. b) Phase-A voltage vector is bigger than other vectors. c) Phase-B voltage vector is bigger than other vectors. d) Phase-C voltage vector is bigger than other vectors.
Fig.4 : The CMVs and their FFTs for two modulation indices.
a) ma = 0.4. b) ma = 0.8.
(a)
(b)
Fig.5 : Experimental setup of 2-level 3-phase inverter system.
Fig.6 :CMVs for two modulation indices. a) ma = 0.4. b) ma = 0.8.
(at and).
(a)
(b)