## Slide 1
Real-Time DC-Link Capacitor Stress Reduction in Two-Level Three-Phase Inverters Using Adaptive Multi-Carrier PWM Method
You may choose either a one-column or two-column format at your discretion
Please print this poster on an A0-sized sheet and bring it to IPEC2026
Enes Ayaz1, Shahriar Sarmast 1, Staffan Norrga1 , Hans-Peter Nee1
1KTH Royal Institute of Technology, Stockholm, Sweden
P1-8-12
Core Idea: Adaptive interleaving between the legs of a single 2L-3Ph inverter reduces DC-link capacitor RMS current without extra hardware.
Introduction
DC-link capacitors are a major reliability bottleneck in industrial power converters.
Ripple current increases ESR losses, hotspot temperature, and degradation.
Conventional single-carrier SPWM cannot actively coordinate switching instants between inverter legs.
Motivation
DC-link capacitors are a major reliability bottleneck in industrial power converters.
Ripple current increases ESR losses, hotspot temperature, and degradation.
Conventional single-carrier SPWM cannot actively coordinate switching instants between inverter legs.
Main Results
up to
27%
lower RMS current
23%
case study
27.6 A -> 21.2 A
~50%
lifetime gain
example estimate
Method: Adaptive multi-carrier PWM
Conventional SPWM uses a common triangular carrier for all inverter legs.
The proposed method assigns individual carriers to each leg and optimizes the phase shifts of legs B and C during each switching period.
Optimization Objective
Measure
phase currents
→
Normalize
current inputs
→
Compute
duty ratios
→
Read compact
LUT
→
Apply carrier
phase shifts
Performance assessment
Simulation Validation