## Slide 1: 1.2 kV Heavy-Duty Electric Vehicle Powertrains: System-Level Analysis and Holistic Efficiency Optimization
Enes Ayaz

## Slide 2: Introduction
The shift towards electrifying heavy-duty vehicles is driven by the increasing need for sustainable transportation solutions to address environmental challenges and reduce emissions.
Power Ratings: Electric trucks require high power ratings.
Megawatt charging systems (MCS) are essential to support rapid charging, aligning with the operational demands of electric trucks.
.
European Union's regulation on driving times
  Drivers may drive for a maximum of 4.5 hours continuously.
  After 4.5 hours, a driver must take a minimum 45-minute rest.
Limitations of 400–800 V architectures:

## Slide 3: Research Motivation & Problem Statement
Research gap
Literature mostly:
  Subsystem-level
  Focused on passenger EVs (≤ 800 V)
Lack of:
  Unified HDV-scale analysis (> 1 kV)
The research objective
Quantify the system-level impact of increasing DC-link voltage from 800 V to 1200 V in heavy-duty electric vehicles.
Key questions
What are performance improvements enabled by increasing the DC-link voltage from 800 V to 1200 V at the system level?
What new penalties and constraints (losses, stresses, sizing) are introduced by high-voltage operation?
Under which design conditions does a 1200 V architecture become preferable to an 800 V system?

## Slide 4: System Overview & Methodology
Studied system
  Battery + charging
  Traction inverter
  Traction motor
Methodology
  Unified virtual-prototyping framework
  Equal-power & equal-loss benchmarking
  Analytical & experimental approach

## Slide 5: Battery & Fast-Charging Analysis
Total energy storaged:
Higher voltage → lower current:
(Preserving the same total energy.)
The instantenous charging current:
The corresponding cable conduction loss :
Power is scaled by:
(while keeping the same conductor area.)
Conduction loss is scaled by:
(if cable current is fixed.)
Cable cross section can be reduced :

## Slide 6: Battery & Fast-Charging Analysis
Main findings:
Same energy : higher voltage → lower current
~33% current reduction at 1200 V
~56% reduction in I²R cable losses
~40–45% cable mass reduction
Full compatibility with MCS standards(> 1 MW)

## Slide 7: Traction Inverter Benchmark
.
Benchmark setup
800 V (1.2 kV SiC) vs 1200 V (2 kV SiC)
Same power, same thermal limits
Loss modeling
  Conduction vs switching
Device Rating
  Die-area optimization
Cooling System
  Cooling-system performance index
DC-Link Capacitance
  Capacitance value and volume
Design Selection
  Efficiency map

## Slide 8: Traction Inverter Loss Calculation
where duty cycles (D(θ)), switch current (ids(θ)), conduction angles (θC1 to θC2), and on-state resistance (rds) are required.
Conduction Loss
where kr and αr are technology-dependent coefficients.
The on-state resistance depends on the voltage rating (UB) and die area (Adie) that can be roughly calculated:
Switching Losses
The zero current switching energy is reliant on the output capacitance (Coss,Q) and switching voltage (Udc).
The overlapping energy aligns with a second order polynomial:
Where θSW1 and θSW2 are switching angles, Esw,zcs and Esw,overlap are zero current switching energy and overlapping energy.

## Slide 9: Traction Inverter Loss Calculation
The voltage and current slew rates determine coefficients α1 and α2s during the switching transitions.
While faster transitions reduce α1 and α2 but aggravate electromagnetic interference (EMI) and common-mode voltage stress.

## Slide 10: Cooling System & DC-Link Capacitance
The junction-to-case thermal resistance decreases with die area
The required heatsink-to-ambient thermal resistance to limit junction temperature:
The heatsink volume is then estimated from the cooling system performance index (CSPI):
The instantaneous dc-link capacitor current is expressed as
The minimum required dclink capacitance for a specified voltage ripple ∆V pp is calculated a
At constant power, a higher dc-link voltage proportionally reduces the capacitor ripple current, thereby decreasing the required capacitance and volume

## Slide 11: Loss Analyses: Switching Frequency & Die Area
.

## Slide 12
.
Results: Cooling System & DC-Link Capacitance

## Slide 13: Traction Inverter: Loss & Power Density Trade-Offs
.
Key results
Similar efficiency (~99.2%)
Lower current ≠ automatically lower losses
1200 V → smaller DC-link capacitor
Power density increased by 11%

## Slide 14: Traction Motor Loss Analyses
.
The same motor geometry and electromagnetic design are maintained.
A higher dc-link voltage is accommodated by reconnecting the existing parallel winding paths in series.
Impedance-based loss factor Φ(ω)
Key insight
  Same harmonic losses: scaled loss factor and voltage levels.
  Slight copper-loss increase : higher insulation requirements typically mandate thicker groundwall and turn insulation.

## Slide 15: Common-Mode Voltage & Bearing Stress
.
Concern : Higher Vdc → higher CMV amplitude
Bearing Voltage Ratio (BVR) quantifies the coupling of CMV to the rotor shaft:
In higher-voltage machines, shielding materials can be employed to further reduce the bearing voltage ratio (BVR), while reinforced insulation decreases the winding-to-rotor capacitance (Cwr).

## Slide 16: Holistic Optimization: Switching Frequency
.
Why holistic?
Inverter losses ↑ with fsw
Motor harmonic losses ↓ with fsw

## Slide 17: Experimental Validation: B2B Setup
.

## Slide 18: Experimental Validation : Loss Seperation

## Slide 19: Experimental Validation: Effiency and Paremeters
Equivalent output capacitance matches datasheet-based output energy
Switching-loss parameters show good agreement with the analytical model (8%–20% deviation)
Total loss estimation agrees with experiments (error < 10%)

## Slide 20: Conclusion
1200 V is not merely a voltage increase; it fundamentally reshapes the entire powertrain architecture, rather than optimizing individual subsystems.
At the charging level, higher DC-link voltage enables megawatt-class fast charging with substantially reduced current, lower cable losses, and significant reductions in cable mass, making compliance with MCS and long-haul operational constraints feasible.
At the inverter level, higher voltage operation reduces current stress and DC-link capacitor requirements. When semiconductor die area and switching frequency are properly optimized, comparable efficiencies to 800 V systems are achieved, while enabling higher power density.
At the system level, a holistic optimization, jointly considering inverter losses, motor harmonic losses, and switching frequency, reveals optimal operating regions that cannot be identified using inverter-only or motor-only design approaches.
This work provides experimentally validated design guidance for next-generation heavy-duty electric vehicles, bridging analytical modeling and high-power laboratory validation, and establishing a practical framework for future high-voltage powertrain development.

## Slide 21: Limitations & Future Work
.
Limitations
Single topology (2-level)
Only rated operating point , no drive-cycle weighting
No lifetime/aging modeling
Limited CMV/motor harmonic loss experimental validation
Future work can be
3-level topologies (NPC / T-type)
Drive-cycle-based optimization
Reliability & lifetime (SiC + capacitors)
CO₂ & life-cycle cost optimization
EMI / CMV experimental campaigns

## Slide 22: Thank you !!!
Research leading to these results has received funding from the EU CHIPSJoint Undertaking under grant agreement no 101007326 (project PowerizeD) and from the (Swedish) partner national funding authority Vinnova. Funding for this research has also been received from the Swedish Energy Agency through the HEMIZERO project.