## Slide 1: Stacked Poly-Phase Bridge
Enes Ayaz

## Slide 2: Why raise the traction DC-link voltage?
Lower current
for the same transmitted power
Smaller conductors
and lower cable losses
Faster charging
with lower current at megawatt power
Challenge
A conventional two-level inverter exposes every switch to the full DC-link voltage.

## Slide 3: SPB portions one high-voltage DC link across N cells
Vcell ≈ Vdc / N
nominal voltage per cell
Series on the DC side
The cells share the total blocking voltage.
Separate winding groups
Each cell controls a three-phase section of the same machine.
The machine and converter become one modular architecture.

## Slide 4: Voltage portioning opens lower device-voltage classes
3 cells
400 V
nominal cell voltage
650 V class
6N = 18
active switches
5 cells
240 V
nominal cell voltage
350 V class
6N = 30
active switches
8 cells
150 V
nominal cell voltage
200 V class
6N = 48
active switches
15 cells
80 V
nominal cell voltage
100 V class
6N = 90
active switches

## Slide 5: Voltage portioning opens lower device-voltage classes

## Slide 6: Lower-voltage GaN can improve device-level performance
Why it matters
Lower RDS(on)
can reduce conduction loss and chip area
Lower charge
can support faster switching and smaller passives
Commercial reality
Current rating, Coss, package parasitics, dynamic RDS(on), and thermal limits can reverse a simple FOM ranking.

## Slide 7: Figure-of-merit of Off-the-shelf GaN Devices

## Slide 8: The optimum cell count balances efficiency against complexity
Voltage benefit
Vcell falls approximately with 1/N
Hardware penalty
Switch count grows linearly as 6N
More cells
lower Vcell
more switches
Core question:
How many stacked two-level cells are worth adding before device count and control overload dominate?

## Slide 9: SPB optimization spans the converter and the machine
Semiconductors
Conduction, Coss/Eoss, overlap loss, current capability
DC-link
Capacitance, ripple, balancing stability, overshoot
Machine
Winding-group count, voltage demand, coupling, harmonics
Integration
Gate drives, isolation, cooling, interconnects, packaging
One common objective: minimum system loss, mass, volume, and implementation risk

## Slide 10: Preliminary results - comparison

## Slide 11: SPB research - milestones