## Slide 1
Multi frequency modulation method
Multi-frequency output with f1,f2,f3 and their higher order harmonics
Requires multi-level converter or SHEPWMs with look-up table
Multi frequency output with complex frequencies stemmed from the multiplication
Requires two-level converter

## Slide 2
Time domain multiplication
Frequency domain convolution
Also it can be formulated considering duty cycle

## Slide 3
 | 0 | f1 | f2 | 2f1 | 2f2 | 3f1 | 3f2 | 4f1 | 4f2
PWM1 | A0 | A1 | - | A2 | - | A3 | - | A4 | -
PWM2 | B0 | - | B1 | - | B2 | - | B3 | - | B4
PWMres = PWM1 x PWM2
 | 0 | f2-f1 | f1 | f2+f1 | f2 | 2f1-f2 | 2f1 | 2f2-f1 | 2f2 | 2f1+f2 | 3f1 | 3f1-f2 | 2f2+f1
PWMres | A0x B0 | A1/2 X B1/2 | A1 X B0 | A1/2 X B1/2 | A0 X B2 | A2/2 X B1/2 | A2/2 X B0 | A2/2 X B1/2 | A0 X B2 | A2/2 X B1/2 | A3/2 X B0 | A3/2 X B1/2 | A1/2 X B2/2

## Slide 4
For example, we want to utilize frequencies of 50 kHz, 120 kHz, and 180 kHz with magnitudes of Fa, Fb, Fc.
Assume that unknown pulses with frequencies of f1 , f2, and f3.
Select which resultant frequencies , from convolution, is selected as the desired frequencies of 50kHz, 100kHz, and 200kHz.
f1=50 kHz
f2+f1=120 kHz
f3+f1=180 kHz
      f1=50kHz
      f2=70kHz
      f3=130 kHz
      Fa=A1
      Fb=A1/2+B1/2
      Fc=A1/2+ C1/2