## Slide 1
Topology | Module connection | Winding requirement | Modulation | Main benefit | Main issue
Dual 3-phase | Two 3-phase GaN VSIs | Two isolated 3-phase sets | Interleaved SVPWM/SPWM | Lower capacitor ripple and fault tolerance | Winding coupling and current sharing
SPB | DC-side series modules | One winding set per module | Phase-shifted carrier PWM + voltage balancing | Low-voltage GaN in high-voltage drive | Capacitor-voltage stability
PPB / segmented | DC-side parallel modules | Segmented or polyphase windings | Group-based interleaving | Capacitor reduction and scalability | Parasitic-sensitive ripple cancellation
Open-end winding | Two inverters per winding set | Open-ended stator winding | Dual-inverter PWM | Multilevel output and high voltage utilization | Circulating current and CMV
Full-bridge modular | H-bridge per phase/coil | Open phase or coil terminals | Bipolar/unipolar PWM | Strong modularity and fault isolation | Higher device count
Balanced inverter | Complementary winding sets | Symmetric dual windings | Complementary PWM | CMV cancellation | Sensitive to timing mismatch