## Slide 1
Agentic AI Optimizer
for Stacked Polyphase Bridge GaN Voltage-Class Selection
Efficiency · thermal feasibility · power density · cost · implementation complexity
650 V
300 V
200 V
100 V
From datasheets to Pareto-optimal SPB architectures
Prepared as a project plan and slide-ready system architecture

## Slide 2
Why this needs an agentic workflow
The best GaN voltage class is not a device-only question.
Core trade-off
Few cells
650 V GaN
+ fewer auxiliaries
+ simpler layout
– higher device stress
– higher RDS(on)
More cells
100–200 V GaN
+ lower device loss
+ smaller voltage step
– many drivers
– more capacitance / PCB
System optimum
η, W/L, €/kW,
thermal margin, reliability
Rule of the project
LLM agents decide what to evaluate, extract uncertain data, select models, and critique assumptions. Deterministic Python/MATLAB functions perform all numerical calculations.
2 | Agentic AI SPB optimizer

## Slide 3
Agent structure
A modular workflow from datasheets to ranked SPB designs, including machine-loss-aware fsw optimization.
Datasheet
Agent
Topology
Agent
Semi Loss
Agent
Machine Loss
Agent
Thermal
Agent
DC-link + Aux
Agent
PCB
Agent
Cost
Agent
Optimizer
+ Critic
Orchestrator AI
controls task order, asks for missing data, calls tools, stores confidence
Outputs: Pareto fronts · optimal fsw per voltage class · ranked architectures · BOM · uncertainty bands
3 | Agentic AI SPB optimizer

## Slide 4
Inputs and standardized databases
Each value carries source, conditions, units, and confidence.
GaN device DB
VDS, RDS(on)(T), Qg, Qoss/Eoss, Coss(V), RθJC, package, price
Operating profile
Vdc range, phase current, modulation, fsw bounds, speed/torque points, coolant temperature
Hardware libraries
capacitors, gate drivers, isolated DC/DC, sensors, connectors, PCB stack-up, cooler options
Design policies
voltage derating, thermal margin, ripple limit, clearance/creepage, acoustic/EMI limits, max cell count
Recommended data object
parameter = { value, unit, test_conditions, source, extraction_method, confidence, uncertainty }
4 | Agentic AI SPB optimizer

## Slide 5
Missing datasheet data strategy
The agent estimates missing values only with traceable fallback models.
1
Measured Eon/Eoff curves
High confidence
2
Waveform integration ∫vDS·iD dt
Medium–high
3
Qgd + gate-drive model
Medium
4
Coss/Qoss/Eoss model
Medium for capacitive loss
5
Similar-device regression
Low; must be flagged
Critic checks
• double-counted Eoss?
• extrapolated current/voltage?
• same package/process?
• uncertainty propagated?
• missing test temperature?
5 | Agentic AI SPB optimizer

## Slide 6
Calculation pipeline
Every candidate architecture and switching-frequency candidate passes through the same deterministic model chain.
Topology
Ncell, Vcell, device class
Loss
conduction + overlap + Coss + gate vs fsw
Thermal
Tj iteration and Nparallel
Implementation
machine loss, DC-link, drivers, PSU, PCB
System score
ηtotal, W/L, €/kW, risk
Important feedback loops
RDS(on)(Tj) → loss → Tj; fsw ↑ → semiconductor switching loss ↑ but machine harmonic loss ↓; cell count → drivers/PSUs/PCB area; capacitance → volume/cost/ripple.
6 | Agentic AI SPB optimizer

## Slide 7
Thermal sizing and parallel-device selection
The number of parallel GaNs is an optimization output, not a fixed assumption.
Assume
Tj
RDS(on)(Tj)
+ switching loss
Thermal network
RθJC + TIM + cooler
Update
Tj
Stop when
|ΔTj| < tolerance
Constraint examples
Tj < 125–150 °C
Tj,max margin ≥ 25 °C
Current sharing derating
Cooler heat-flux limit
Decision
Choose minimum Nparallel satisfying thermal constraints across mission profile.
7 | Agentic AI SPB optimizer

## Slide 8
DC-link, auxiliary circuits and layout estimation
System-level volume can overturn semiconductor-only conclusions.
DC-link Agent
Simulate cell power pk(t)
Estimate ΔVC and IC,rms
Select capacitor count
Calculate ESR loss, volume, cost
Gate + PSU Agent
Pg = NswQgVgfsw; fsw also affects aux/cooling
Driver and isolated supply
Isolation channels
Auxiliary loss and volume
PCB/Layout Agent
Parametric bridge cell
spacing + creepage rules
decoupling loop area
rough width × height profile
Estimated converter volume = semiconductors + capacitors + cooler + PCB + auxiliaries + busbar/connectors; fsw can reduce machine/filter burden but increases switching heat
8 | Agentic AI SPB optimizer

## Slide 9
Optimization formulation
Search the design space and report the Pareto front, not only one winner.
Design variables
Ncell
GaN voltage class
Nparallel
fsw
modulation
cell capacitance
thermal solution
PCB layout factor
Objectives
maximize total efficiency ηtotal
minimize inverter + machine loss
maximize power density kW/L
minimize cost €/kW
maximize robustness
Constraints
voltage derating
thermal margin
DC-link ripple
capacitor RMS current
clearance/creepage
EMI/acoustic limits
package current limit
available components
Recommended optimizer: start with NSGA-II; sweep or co-optimize fsw; add Monte Carlo uncertainty to compare robust designs.
9 | Agentic AI SPB optimizer

## Slide 10
Expected outputs and validation plan
The deliverable should be useful both for publication and hardware planning.
Pareto plots
ηtotal vs W/L vs €/kW for each voltage class and optimal fsw
Ranked designs
best efficiency, best density, best cost, best robust choice, best fsw window
BOM + footprint
devices, capacitors, drivers, PSUs, sensors, estimated PCB/cooler size
Assumption report
missing data, surrogate models, uncertainty, critic-agent warnings
Validation sequence
1) datasheet extraction check → 2) double-pulse test for selected GaNs → 3) thermal bench test → 4) SPB cell prototype → 5) full system comparison
10 | Agentic AI SPB optimizer

## Slide 11
Suggested implementation roadmap
Build the tool in layers so every result remains traceable and fsw-dependent losses are not hidden.
Phase 1
Database + datasheet parser
GaN, capacitors, drivers, DC/DC supplies
Phase 2
Deterministic models
loss, thermal, DC-link ripple, auxiliary loss
Phase 3
Optimizer + uncertainty
NSGA-II, Monte Carlo, confidence scoring
Phase 4
Validation + paper figures
DPT, thermal test, Pareto plots, final ranking
Main principle
Every reported design should include numbers, sources, assumptions, and confidence — so the result is defensible, not just optimized.
11 | Agentic AI SPB optimizer

## Slide 12
Switching frequency + machine-loss agent
fsw is a design variable because it trades semiconductor switching loss against machine harmonic loss.
Ptotal(fsw) = Psemi,cond + Psemi,sw(fsw) + Pmachine,harm(fsw) + Paux + Pcap
Inputs
• fsw range and modulation
• speed–torque operating points
• machine Ld, Lq, Rs and flux
• harmonic loss map / FEA / test data
• allowed ripple, EMI and acoustic limits
Trade-off model
• fsw ↑ reduces current ripple and voltage harmonics
• machine copper/iron harmonic loss decreases
• GaN switching, Coss and gate losses increase
• cooling volume can increase at high fsw
• optimum differs by voltage class
Outputs
• optimal fsw window for each architecture
• inverter-only vs system-level optimum
• ηtotal = inverter + machine efficiency
• robustness under missing datasheet data
• constraint violations and assumptions
Key message: compare each GaN voltage class at its own system-optimal fsw, not at one fixed switching frequency.
12 | Agentic AI SPB optimizer