## Slide 1: PhD Works
Enes Ayaz

## Slide 2: Outline
The Effects of the Busbar and Battery Parasitic Inductances
Conventional Back-to-Back Inverter Setup
Intelligent Gate Driver Measurement Unit: Online Measurement
ECCE-Europe Paper Digest

## Slide 3: Simplified Inverter Model
We do not consider output harmonics for the phase currents
Combined Inverter and battery model
The inverter can be modeled as current sources of harmonic components.

Leg current in the frequency domain is the convolution of the phase current and switching function.

## Slide 4: The Aim of Using Impedance Model
A simplified model does not provide the effective capacitance values for each phase.
Additionally, a resonant structure is created because of the capacitors and stray inductances, which create high impedance for some frequencies.
High impedance points

## Slide 5: Busbar Geometry 62mm Power Module
Capacitor
Power Modules
DC- Nodes
DC+ Nodes
C1
C2
C3
C4
 | Leg A | Leg B | Leg C
Capacitor-1 |  |  | 
Capacitor-2 |  |  | 
Capacitor-3 |  |  | 
Capacitor-4 |  |  | 
 | Leg A | Leg B | Leg C
Capacitor-1 |  |  | 
Capacitor-2 |  |  | 
Capacitor-3 |  |  | 
Capacitor-4 |  |  | 
Step response of capacitors to each leg
The response of capacitor A for each leg should be calculated as:
+

## Slide 6: DC Link Current (Positive/Negative/Zero Sequences)
6th 12th

## Slide 7: Without Battery Model
Capacitor Responses to Phase-A
Capacitor-1 Response to All-phases

## Slide 8: The Effect of the Battery Connection
Low frequency resonance
High frequency
resonance
Capacitor-1 Response to All-phases
Low frequency resonance
High frequency
resonance
Capacitor Responses to Phase-A

## Slide 9: High Frequency Resonance
14 kHz Switching
24kHz Switching
Harmonic number
Harmonic number
P.S: The high-frequency resonance might be considerable if we have a dual-3-phase-inverter (6-phase) structure and we desire to interleave them to reduce capacitance requirements. (We should look at phase-response (not magnitude response) at such a scenario)

## Slide 10: Low Frequency Resonance
700 Hz Fundamental
200 Hz Fundamental

## Slide 11: Parasitic Inductances (Switching Speed Limitation)
Parasitic Sources | Inductance
Power module | 50 nH
Capacitor ESL | 50nH
Busbar | Overall <20nH

## Slide 12: Parasitic Inductances (Switching Speed Limitation)
Maximum Current (MaxA) (inA) | dv/dt (in V/nS) @ MaxA | Overshoot (in %) @ MaxA
380 A | 35 V/ns | 40 %
Phase-A Current
Phase-B Current
Phase-C Current
Drain-source Voltage
Leg-A
Bottom Switch

## Slide 13: Outline
The Effects of the Busbar and Battery Parasitic Inductance
Conventional Back-to-Back Inverter Setup
Intelligent Gate Driver Measurement Unit: Online Measurement
ECCE-Europe Paper Digest

## Slide 14: Back-to-Back Inverter
Iph
Vph1
Vph2
When two AC voltage sources are connected through an inductance, the power flow between them depends on the phase difference between the voltages of the two sources and the reactance of the connecting inductance.
Y. Luo, "A Variable Power Factor High Power Testbed for Traction Inverter Using Back-to-Back Connection,"
Q

## Slide 15: Inverter Losses
In a two-level inverter, we can assume the losses do not depend on the power factor.
We can control the modulation index and the current, then we can estimate the power loss for the desired operating points.
The efficiency can be estimated then using the power loss and operating point power.
50% of power
100% of power
25% of power
2000
4500
2500
Torque [Nm]
Power [kW]
600
speed [rpm]
6000
100% of power
Dp1
Dp2
Dp3
Dp4
Dp5
Dp6
50% of power
0

## Slide 16: Phase-Shift Control
Controlling the current and apparent power. We do not have active control on power factor.

## Slide 17: Outline
The Effects of the Busbar and Battery Parasitic Inductance
Conventional Back-to-Back Inverter Setup
Intelligent Gate Driver Measurement Unit: Online Measurement
ECCE-Europe Paper Digest

## Slide 18: Intelligent Gate Drivers: Online Measurement
Indicator of Device Health:
  ​ increases with gate-oxide degradation, bond-wire faults, and thermal aging, serving as an early warning for failure.
  Example: A 15–125% rise in ​ precedes SiC MOSFET failure.
Fault Prevention:
  Detects chip- and package-level defects (e.g., solder cracks, oxide traps) before catastrophic failure.
Fig: Intelligent Gate Drivers:
Sensing,control, gate drivers
High-frequency current injection could be utilized to isolate ​​ from load current, avoiding synchronization and phase-shift errors of the measurement.
F. Karakaya, "An Approach for Online Estimation of On-State Resistance in SiC MOSFETs Without Current Measurement,
Jochen Henn, ”Intelligent Gate Drivers for Future Power Converters”

## Slide 19: Outline
The Effects of the Busbar and Battery Parasitic Inductance
Conventional Back-to-Back Inverter Setup
Intelligent Gate Driver Measurement Unit: Online Measurement
ECCE-Europe Paper Digest

## Slide 20: Common-Mode Voltage Reduction in Two-Level Inverters by Introducing Adaptive Carrier-Phase-Shift Method

## Slide 21: Common-Mode Voltage Reduction in Two-Level Inverters by Introducing Adaptive Carrier-Phase-Shift Method