## Slide 1: Thermal Modelling
[1] Electrothermal-Control Co-Design of an All Silicon Carbide 2×250 kW Dual Inverter for Heavy-Duty Traction Applications
The thermal model, including just thermal resistance, is enough to calculate steady-state junction temperature and losses for continuous power operation.
[2] ANALYSIS AND MODELING OF A LIQUID COOLED HEAT SINK FOR EV TRACTION INVERTER SYSTEMS
A Foster network is required to consider peak power operation for a finite time.
[3] A SiC-Based Liquid-Cooled Electric Vehicle Traction Inverter Operating at High Ambient Temperature
Continuous rating​
600 kW ​
Short term rating​
20% above the continous rating​
10 s

## Slide 2: Thermal Modelling
[4] MSCSM70AM10CT3AG Datasheet Phase Leg SiC MOSFET Power Module https://www.microchip.com/content/dam/mchp/documents/PPM/ProductDocuments/DataSheets/Microsemi_MSCSM70AM10CT3AG_Phase_Leg_SiC_MOSFET_Power_Module_Datasheet_1.0.pdf
Time constant
[2] ANALYSIS AND MODELING OF A LIQUID
COOLED HEAT SINK FOR EV TRACTION INVERTER SYSTEMS
Time constant

## Slide 3: Overall Modelling
Rating calculations (Continous)
Modulations
SPWM
THIPWM
  1/6 THIPWM
  ¼ THIPWM
SVM
DPWM

## Slide 4
Modulation
Function
Input :
ma : modulation index
pn : pulse number (carrier to fundamental ratio )
npoints: number of sampling points during fundamental signal (determine the time steps)
carrytype: Type of carrier signal (two options)
        'sawp' : sawtooth carrier with positive slope
        'tria' : triangular carrier (default)
smp: (optional) reference sampling mode (three options)
        'ns' : natural sampling (default)
        'rs' : regular symmetric sampling
        'ra' : regular asymmetric sampling
cmode: (optional) reference common-mode component for three-phase systems
        'none' : No common mode (default)
        'tri4' : One fourth third harmonic
        'tri6' : One sixth third harmonic
theta0: (optional) reference phase offset
thetac: (optional) carrier phase offset
start: (optional) reference angle to start with (default=0)
end: (optional) reference angle to end with (default=2pi)
ma0: (optional) DC reference (default =0)
Output:
s: Pwm pattern during fundamental cycle
wt: (optional) phase angle vector corresponding to s
carr: (optional) carrier signal vector
ref: (optional) reference signal vector
ma
pn
npoints
carrytype
smp
cmode
theta0
thetac
start
end
ma0
s
wt
carr
ref

## Slide 5: SCPAR (Semicondcutor and Thermal Parameters)
SCPAR.SW.TOF.T
SCPAR.SW.TOF.I
SCPAR.SW.TOF.E
SCPAR.SW.TOF.U
SCPAR.SW.TOF.model
SCPAR.SW.TON.T
SCPAR.SW.TON.I
SCPAR.SW.TON.E
SCPAR.SW.TON.U
SCPAR.SW.TON.model
SCPAR.SW.ON.T
SCPAR.SW.ON.I
SCPAR.SW.ON.V
SCPAR.SW.ON.model
SCPAR.SW.NAME
SCPAR.SW.Manuf
SCPAR.SW.RATG.Irat
SCPAR.SW.BV
SCPAR.SW.TH.Rthjc
SCPAR.SW.TH.Rthch
SCPAR.SW.TH.model
SCPAR.SW.NPKG
SCPAR.SW.Package
SCPAR.HSSW.NAME
SCPAR.HSSW.L
SCPAR.HSSW.Rthha
SCPAR.HSSW.model
SCPAR.HSDI.NAME
SCPAR.HSDI.L
SCPAR.HSDI.Rthha
SCPAR.HSDI.model
SCPAR.igbtareascale
SCPAR.diodeareascale
SCPAR.DI.TOF.T
SCPAR.DI.TOF.I
SCPAR.DI.TOF.E
SCPAR.DI.TOF.U
SCPAR.DI.TOF.model
SCPAR.DI.ON.T
SCPAR.DI.ON.I
SCPAR.DI.ON.V
SCPAR.DI.ON.model
SCPAR.DI.NAME
SCPAR.DI.Manuf
SCPAR.DI.RATG.Irat
SCPAR.DI.BV
SCPAR.DI.TH.Rthjc
SCPAR.DI.TH.Rthch
SCPAR.DI.TH.model
SCPAR.DI.NPKG
SCPAR.DI.Package

## Slide 6: PC and OP
PC.SC.diodepackincr
PC.SC.Igbtpackincr
PC.SC.Igbtcoolincr
PC.SC.diodecoolincr
PC.SC.seriesautoselect
PC.SC.Nseries
PC.SC.diodefile
PC. SCTHERM.Tjtol
PC. SCTHERM.model
PC. SCTHERM.maxiter
PC.npar
PC.nop
PC.TOPOLOGY
OP.Ta
OP.Ud
PC.SC.seriesmargin

## Slide 7
Modulation
Function
Input
Parameters for calculations
Dataset
(Semiconductor and Heatsink)
scloss
PC
OP
SCPAR
ip
vp
f1
PC.TOPOLOGY
(switch case)
1
2
3
4
5
case for 2l
case for 3l NPC
case for 3l ANPC
case for MMC
case for MMC
scloss2l
Loss Calculation
Function
Loss Calculation
Function for 2L
SCLOSS

## Slide 8: 1. Calculating the number of series IGBTs and Diodes
PC.SC.seriesautoselect
PC.SC.seriesmargin
PC.SC.Nseries
SCPAR.DI.NPKG
SCPAR.SW.NPKG
If PC.SC.seriesautoselect =0
determine # of series IGBTs (N) by PC.SC.Nseries
Then # of series diodes (Nd) N * SCPAR.DI.NPKG / SCPAR.SW.NPKG
If PC.SC.seriesautoselect =1
determine PC.SC.seriesmargin
and # of series IGBTs (N) by PC.SC.seriesmargin *2*max(OP.Ud)/SCPAR.SW.BV
Then # of series diodes (Nd) N * SCPAR.DI.NPKG / SCPAR.SW.NPKG
Why do we multiply by 2 ?
if we select margin as 1.5, we have a DC link 1250 Voltage and semiconductor with 1200V blocking voltage, our series devices become 3.
Using 3 series device seem not logical?
if isfield(PC.SC,'seriesautoselct')
if PC.SC.seriesautoselct,
N = round(PC.SC.seriesmargin * 2*max(OP.Ud)/SCPAR.SW.BV);
else
N=PC.SC.Nseries;
end;
end
Nd = N*SCPAR.DI.NPKG/SCPAR.SW.NPKG; % no of diodes

## Slide 9: 1. Temperature Tolerance and SCLOSS struct
T0=1/f0; % Fundamental cycle time
thiterate = PC.SCTHERM.model > 1; % Iterate to find proper junction temperatures?
if thiterate, PC.SCTHERM.Tjtol=0.5; end; %tolerance in temperature;
npts=length(Up); % No of time points
PC. SCTHERM.model
PC. SCTHERM.Tjtol
PC. SCTHERM.maxiter
% Reserve space
SCLOSS.SW.Tj = plstruc('Switch junction temperature',zeros(PC.npar,PC.nop),'C',1);
SCLOSS.SW.Pc = plstruc('Switch conduction losses',zeros(PC.npar,PC.nop),'W',1);
SCLOSS.SW.Pton = plstruc('Switch turn on losses',zeros(PC.npar,PC.nop),'W',1);
SCLOSS.SW.Ptof = plstruc('Switch turn off losses',zeros(PC.npar,PC.nop),'W',1);
SCLOSS.SW.Ptot = plstruc('Switch total losses',zeros(PC.npar,PC.nop),'W',1);
SCLOSS.DI.Tj = plstruc('Diode junction temperature',zeros(PC.npar,PC.nop),'C',1);
SCLOSS.DI.Pc = plstruc('Diode conduction losses',zeros(PC.npar,PC.nop),'W',1);
SCLOSS.DI.Ptof = plstruc('Diode turn off losses',zeros(PC.npar,PC.nop),'W',1);
SCLOSS.DI.Ptot = plstruc('Diode total losses',zeros(PC.npar,PC.nop),'W',1);
SCLOSS.Ptot= plstruc('Total semiconductor losses',zeros(PC.npar,PC.nop),'W',1);

## Slide 10: Creating Loop for different operation point and area scales
% Check dimension of voltage and current vectors
if size(Up,1) == PC.npar*PC.nop
varsizeopt =1; % option 1
elseif size(Up,1) == PC.npar
varsizeopt =2; % option 2
elseif size(Up,1) == 1
varsizeopt =3; % option 3
else
error('Wrong dimension of ')
end
PC.npar is related to the selection of igbtareascale/diodearescale SCPAR.igbtareascale SCPAR.diodeareascale
PC.nop is related to the selection of operating condition OP.Ta OP.Ud
% Extract vectors with phase current and voltage for this point
switch varsizeopt
case 1
varindex = kop+(kpar-1)*PC.nop;
case 2
varindex = kpar;
case 3
varindex = 1;
end
Ipk = Ip(varindex,:);
Upk = Up(varindex,:);
We should update the plot script as well
PC.npar=length(SCPAR.diodeareascale);
PC.nop=length(OP.Ud);

## Slide 11: Finding devices currents and commutations
sw = (Ipk>=0&Upk>0) | (Ipk<0&Upk<=0); % =1 when current passes through switch
di = ~sw; % =1 when current passes through diode
Isw = abs(Ipk.*sw); % current through switch
Idi = abs(Ipk.*di); % current through diode
comm = sw - [sw(end) sw(1:end-1)]; % Nonzero at commutations (NOTE includes natural as well as forced commutations)
s2d=find(comm < -eps); % Find the instants (samples) when current commutates from switch to diode
d2s=find(comm > eps); % Find the instants (samples) when current commutates from diode to switch
is2d = abs(Ipk(s2d)); % Current at commutations switch to diode
id2s = abs(Ipk(d2s)); % Current at commutations diode to switch
Tjdi = OP.Ta(kop); % Inital junction temp value for iteration
Tjsw = OP.Ta(kop); % Inital junction temp value for iteration
niter=0;
go=1;

## Slide 12: Thermal iteration-Loss Calculation
Pcsw = Isw*Von(SCPAR.SW.ON,Tjsw,Isw/SCPAR.igbtareascale(kpar))/npts/2; % '/2' -> Loss in one of two devices in a phase leg
Pcdi = Idi*Von(SCPAR.DI.ON,Tjdi,Idi/SCPAR.diodeareascale(kpar))/npts/2;
Ptonsw = SCPAR.igbtareascale(kpar)*sum(swloss_calc(SCPAR.SW.TON , Tjsw , 2*OP.Ud(kop)/N , id2s/SCPAR.igbtareascale(kpar))) / T0 / 2;
Ptofsw = SCPAR.igbtareascale(kpar)*sum(swloss_calc(SCPAR.SW.TOF , Tjsw , 2*OP.Ud(kop)/N , is2d/SCPAR.igbtareascale(kpar))) / T0 / 2;
Ptofdi = SCPAR.diodeareascale(kpar)*sum(swloss_calc(SCPAR.DI.TOF , Tjdi ,2*OP.Ud(kop)/Nd , id2s/SCPAR.diodeareascale(kpar))) / T0 / 2;
Ptotsw = Pcsw + Ptonsw + Ptofsw;
Ptotdi = Pcdi + Ptofdi;

## Slide 14: Thermal Modelling