## Slide 1
Uc-min | 15V
Ip | 300A
Is | 300/2000= 0.15A
Rsmax | 22.5
RMmax | 67.1

## Slide 2
B-Box RJ45 (AINx) LEM LF 310-S (secondary connector)
------------------ -----------------------------------
Pin 1–2 : +15 V ----------------> +UC (sensor +15 V)
Pin 7–8 : –15 V ----------------> –UC (sensor –15 V)
Pin 3 & 6 : 0 V -----------------> 0V (sensor 0 V reference)
Make Vout node with RM:
IS pin ------------------------> one end of RM (this is Vout to the B-Box)
Other end of RM ----------------> 0V
Feed the voltage to the ADC:
Pin 4 : Positive input -----------o---- Vout (node between IS and RM)
Pin 5 : Negative input -----------o---- 0V