## Slide 1: PWM Losses on Motor Side
Enes Ayaz, KTH

## Slide 2: Given Parameters
% Given parameters- For operating point 1
id = -224.33; % d-axis current value in A
iq = 325.97; % q-axis current value in A
vd = -138.8; % d-axis voltage value in V
vq = 94.9; % q-axis voltage value in V
Vdc= 625; % DC link voltage in V
Ld= 62.1e-6; % d-axis inductance value in H
Lq=101e-6; % q-axis inductance value in H
Torque= 600; % Torque of the motor in N.m
RPM = 3000; % Rotational speed in RPM
% Given parameters- For operating point 2
id = -118.36; % d-axis current value in A
iq = 222.25; % q-axis current value in A
vd = -198.3; % d-axis voltage value in V
vq = 175.4; % q-axis voltage value in V
Vdc= 625; % DC link voltage in V
Ld= 66e-6; % d-axis inductance value in H
Lq=146e-6; % q-axis inductance value in H
Torque= 370; % Torque of the motor in N.m
RPM = 5000; % Rotational speed in RPM

## Slide 3: Modulation Parameter Calculation
Angle (rad)
Current (A)
Angle (rad)
Voltage (V)
d-q axis voltage waveforms
d-q axis voltage waveforms
Reverse Park and Clarke Transformation
Reverse Park and Clarke Transformation

## Slide 4: Modulation Parameter Calculation
Voltage (V)
Current (A)
Time (sec)
For operating point 1
Modulation index: 0.5381
Power factor: 0.9329
Electrical Frequency: 300.00 Hz
DC-link Voltage: 625.00 V
Peak phase current: 395.70 A
Load calculation: 0.4143

## Slide 5: Modulated Waveform
Reference Signal (p.u)
Time (sec)
Reference Signal (p.u)
Time (sec)
SPWM
THPWM
Current (A)
Time (sec)
Time (sec)
Time (sec)
Pulsated Phase Voltage (V)
Pulsated Phase Voltage (V)

## Slide 6: Time Domain Inductance Calculation
La = Ld * sin(theta).^2 + Lq *cos(theta).^2;
Lb = Ld * sin(theta-2*pi/3).^2 + Lq *cos(theta-2*pi/3).^2;
Lc = Ld * sin(theta+2*pi/3).^2 + Lq *cos(theta+2*pi/3).^2;
Time (sec)
Phase Inductance ()

## Slide 7: Phase Current Calculations- State Space
i_a= zeros(size(v_phase_a)); % phase-A time domain current vector
i_b= zeros(size(v_phase_b)); % phase-B time domain current vector
i_c= zeros(size(v_phase_c)); % phase-C time domain current vector
time=wt/2/pi/f1; % angle-to-time
sample_time=time(2)-time(1); % sample_time
for t=2:length(time)
dL_dt = (L_a(t) - L_a(t-1)) / sample_time; % Inductance change within sample time
i_a(t) = i_a(t-1) + sample_time * ((v_phase_a(t) - rs*i_a(t-1) - dL_dt * i_a(t-1)) / L_a(t)); % State-Space
dL_dt = (L_b(t) - L_b(t-1)) / sample_time; % Inductance change within sample time
i_b(t) = i_b(t-1) + sample_time * ((v_phase_b(t) - rs*i_b(t-1) - dL_dt * i_b(t-1)) / L_b(t)); % State-Space
dL_dt = (L_c(t) - L_c(t-1)) / sample_time; % Inductance change within sample time
i_c(t) = i_c(t-1) + sample_time * ((v_phase_c(t) - rs*i_c(t-1) - dL_dt * i_c(t-1)) / L_c(t)); % State-Space
end
Current (A)
Time (sec)
Including common mode current since it is solved in a single phase equivalent circuit

## Slide 8: Differential mode current and reconstructing dq axis current
Current (A)
Time (sec)
Park and Clarke Transformation
Current (A)
Time (msec)
q-axis current
d-axis current

## Slide 9: Different Switching Frequencies

## Slide 10: Inverter Losses